## Slide 1: 21CSE251T – Digital Image Processing Unit IV
Concepts on Image Segmentation

## Slide 2: Topics
Region of interest (ROI) selection
Feature extraction: Histogram based features - Intensity Features-Colour - Shape Features-Local Binary Patterns (LBP) - Texture descriptors- Grey Level Occurrence Matrix (GLCM)
Fundamentals of Image Compression models – Error Free Compression – Variable Length Coding –Bit – Plane Coding – Lossless Predictive Coding – Lossy Compression – Lossy Predictive Coding

## Slide 3: Region of Interest (ROI) Selection

## Slide 4: Region of interest (ROI) selection
Region of Interest (ROI) selection is a process where a specific area or subset of an image is identified for further processing.
The entire image may contain irrelevant or redundant information. Instead focusing on a smaller region can improve efficiency and accuracy.
ROI selection is essential in tasks like object detection, tracking, recognition, and analysis
By focusing computational resources on relevant image regions, ROI selection helps improve efficiency, reduce processing time, and enhance accuracy.

## Slide 5: ROI Selection methods
Manual Selection
Automatic Detection
Feature-Based Selection
ROI Tracking

## Slide 6: Manual Selection
A user may manually define the ROI by specifying its boundaries interactively using tools like a mouse or touch interface
  Example: In image editing software, a user might draw a bounding box around the object of interest

## Slide 7: Automatic Detection:
Algorithms are used to automatically detect regions of interest based on predefined criteria or features
  Example: In medical imaging, algorithms may automatically detect and segment specific organs or abnormalities within an image

## Slide 8: Feature-Based Selection
ROI selection can also be guided by specific features or characteristics of the image
Example: In face recognition systems, the ROI might be determined based on facial features such as eyes, nose, and mouth.

## Slide 9: ROI Tracking
In applications involving video or sequential images, the ROI may need to be tracked over time as it moves or changes shape.
Tracking algorithms are used to follow the ROI's movement and adjust its position or size accordingly

## Slide 10: Feature Extraction

## Slide 11: Feature Extraction
Feature extraction is an essential step in many image processing and computer vision tasks, including image classification, object detection, segmentation, and recognition.
The purpose of an image feature is to describe the object in a meaningful manner so as to aid the recognition process and to help in the discrimination of these objects.

## Slide 12: Essential Characteristics of Good features are:
Robustness : The property of a feature’s invariance to operations such as translation, rotation, scaling, illumination, and noise
Discrimination : There should not be any overlapping
Reliability
Independence : The features should be uncorrelated to each other
Resistance to noise
Compactness : The features should be small in number so that they can be represented compactly

## Slide 13: Histogram / Brightness Features (Intensity Feature Descriptors)

## Slide 14: Histogram features
Histogram features are also known as brightness features and are described in terms of the luminance (or intensity) features.
The histogram shows the brightness distribution found in the object.
The first order histogram of an image can be approximated using the below equation
Here,
N(b) is the number of pixels having an amplitude of rb
L is the total grey levels and
m is the total number of pixels in the image.

## Slide 15: First order moments.
First order moments are calculated based on individual pixel values. Some of the features that are helpful include the following.
  Mean
  Standard deviation
  Skewness
  Kurtosis
  Energy
  Entropy

## Slide 16: Mean
Mean of the histogram is given by
=
The mean indicates the brightness of image
L -> Total grey levels in the image.
b -> Intensity value of ith bin.
p(b) -> probability of occurrence of b in image.

## Slide 17: Standard Deviation
Standard deviation indicates the contrast / the spread of data
SD =

## Slide 18: Skewness
Skewness indicates the asymmetry about the mean in the grey level distribution.
Skewness =
A negative skew indicates that the tail is on the left side of the distribution, which extends towards more negative values.
A positive skew indicates that the tail is on the right side of the distribution, which extends towards more positive values.
A value of zero indicates that there is no skewness in the distribution at all, meaning the distribution is perfectly symmetrical.
used to describe the spread and height of your normal distribution.

## Slide 19: Kurtosis
Kurtosis is a measure of the "tailedness" of the intensity distribution.
High kurtosis indicates a sharper peak and heavier tails, while low kurtosis indicates a flatter peak and lighter tails
Kurtosis =

## Slide 20: Energy
Energy is the sum of brightness values of all the pixels present in the object. This is called zero order spatial moment
Energy =
The energy is 1 for an image having a constant intensity and reduces with increased distribution of grey level values

## Slide 21: Entropy
The entropy indicates the minimum number of bits required to code the image.
Entropy = -

## Slide 22: Second Order Moments / Texture Analysis
These are based on joint probability distribution of pixels I and J. The histogram of histogram of the second order distribution is given by
p(a,b)
Where, m is the total number of pixels.
These measures are useful in measuring the texture of images and includes Autocorrelation, Covariance, Inertia, Absolute value, inverse difference, energy and entropy.

## Slide 23: Colour Features

## Slide 24: Colour Features
Colour features are very useful in object characterization. Colour histograms can be obtained for colour images. Some of the features are:
Colour histogram
Histogram Intersection
Colour Coherence Vector

## Slide 25: Colour histogram
Let two histograms of images A and B, be given as follows:
A = and
B =
The similarity between two images is given by colour distance. Colour distance is given by the measure
d =

## Slide 26: Histogram Intersection
The pixels that are common in two images, is given by
I =

## Slide 27: Colour Coherence Vector
For finding colour coherence vector, the image can be partitioned into two parts – one part consisting of a count of pixels that belong to a large uniform region and the other consisting of the pixels that belong to a sparse region.
Colour coherence vector =
Where,
P is the coherent pixel
Q is the incoherent pixel

## Slide 28: Note:
Similar to non-colour images, the mean, the variance, skewness, kurtosis and other moments can be identified and detected for feature extraction from colour images
These image features are mostly used with content-based retrieval systems.

## Slide 29: Shape features

## Slide 30: Shape Feature
Shape features in image processing are descriptors that capture the geometric properties and spatial arrangement of objects or regions within an image
These features provide valuable information about the shape, size, orientation, and compactness of objects, and they are widely used in tasks such as object recognition, classification, segmentation, and tracking.

## Slide 31: Shape region features are
Area
Perimeter
Shape factor (Compactness)
Area to Perimeter ration
Object Length
Object width
Elongated Ness
Aspect Ratio
Rectangularity

## Slide 33: Area
The area of an object is the number of pixels in the object. It is shift invariant. The area of binary image is given by
A =
Area can also be calculated in terms of polygon. Let Q be the polygon. Then the area of Q is given by
A(Q) =
where,
NB is the number of points that lie in boundary
N1 is the number of interior points, not in boundary

## Slide 34: Perimeter
Perimeter of an object is the number of pixels present in the boundary of the object.
Perimeter is shift invariant and rotation invariant.

## Slide 35: Compactness (Shape Factor)
It’s a measure of how closely an object's shape resembles a compact form
Compactness = or

## Slide 36: Circularity (Area to Perimeter ratio)
A measure of how closely an object's shape resembles a circle
Circularity =

## Slide 37: Object Length (major axis)
The longest line that can be drawn through the object connecting the two farthest points in the boundary is called its major axis. If are end points of major axis, then major axis length is given by

## Slide 38: Object Width (minor axis)
It is the largest line that can be drawn through the object while maintaining perpendicular with the major axis. The formula is
are end points of minor axis

## Slide 39: Bounding box Area
The area of the box that completely surrounds an object is called its bounding box area. This is calculated by the formula

## Slide 40: Features Derived from Bounding Box Rectangle

## Slide 41: Local Binary Patterns (LBP)
Local Binary Patterns (LBP) have emerged as a powerful technique for texture description and feature extraction.
First introduced by Ojala, Pietikäinen, and Maenpaa in 1994, LBP has found widespread use in various applications such as facial recognition, texture classification, and object detection due to its simplicity and effectiveness.

## Slide 42: What are Local Binary Patterns?
LBP is a texture descriptor that characterizes the local structure and appearance of an image. It operates by analyzing the relationship between a pixel and its neighboring pixels within a defined neighborhood. This process enables the encoding of texture information by comparing pixel intensities.

## Slide 43: What are Local Binary Patterns?-Cont.
The fundamental idea behind LBP revolves around thresholding. To compute the LBP value of a pixel, a threshold is applied to the intensity values of its surrounding pixels.
The resulting binary pattern is constructed by comparing the intensity of each neighbor with the center pixel. If the neighbor's intensity is greater than or equal to that of the center pixel, it is assigned a value of 1; otherwise, it receives a value of 0.
This sequence of binary values is then converted to a decimal number, creating the LBP code for that pixel.

## Slide 44: LBP Work Process
Selecting a Neighborhood: A key aspect of LBP is the choice of neighborhood for each pixel. Typically, a square neighborhood of a certain radius is considered, encompassing a set of neighboring pixels around the central pixel.
Thresholding and Binary Comparison: Once the neighborhood is defined, the LBP operator computes the binary pattern. It compares the grayscale intensity of the center pixel with that of its neighbors, setting the bit to 1 if the neighbor's intensity is greater than or equal to the center pixel's intensity; otherwise, it assigns a 0.
Building the LBP Code: After performing the comparisons for all the neighbors, the resulting binary sequence is assembled clockwise or counterclockwise to form the LBP code.
Histogram Generation: The LBP codes are then used to construct a histogram, where the frequency of occurrence of different LBP patterns within the image is recorded. This histogram serves as a feature vector representing the texture characteristics of the image.

## Slide 45: Algorithm to Calculate Local Binary Pattern
Steps:
1- Divide the examined window into cells (e.g. 16x16 pixels for each cell).
2- For each pixel in a cell, compare the pixel to each of its 8 neighbors (on its left-top, left-middle, left-bottom, right-top, etc.). Follow the pixels along a circle, i.e. clockwise or counter-clockwise.
3- Where the center pixel's value is greater than the neighbor's value, write "1". Otherwise, write "0". This gives an 8-digit binary number (which is usually converted to decimal for convenience).
4- Compute the histogram, over the cell, of the frequency of each "number" occurring (i.e.,each combination of which pixels are smaller and which are greater than the center)

## Slide 46
5-Optionally normalize the histogram.
6- Concatenate (normalized) histograms of all cells. This gives the feature vector for the window.
Formula/Expression:

## Slide 47: Applications of LBP
LBP has showcased its versatility in various image analysis tasks:
Texture Classification: LBP has been particularly effective in classifying textures in images. Its ability to capture local texture patterns makes it well-suited for tasks like distinguishing between different surface textures in materials.
Facial Recognition: LBP has been widely used in facial recognition systems due to its robustness against illumination changes and facial expressions. By extracting discriminative features from facial images, LBP contributes significantly to accurate face recognition.
Object Detection: In combination with other techniques, LBP aids in object detection by extracting texture features that contribute to identifying objects within images.

## Slide 48: Challenges and Advancements
While LBP presents several advantages, including computational simplicity and robustness, it also faces certain limitations. One of the main challenges lies in its sensitivity to noise and variations in illumination.
To address these challenges, researchers have proposed various improvements and extensions to the basic LBP algorithm. These include uniform patterns, rotation-invariant LBP, and the use of different neighborhood structures to enhance its robustness and discriminative power.

## Slide 49
GREY LEVEL OCCURRENCE MATRIX (GLCM)

## Slide 63
FUNDAMENTALS OF IMAGE COMPRESSION MODELS

## Slide 64: Image Compression
Introduction, coding Redundancy
Inter-pixel redundancy, image compression model
Lossy and Lossless compression
Huffman Coding, Arithmetic Coding
LZW coding, Transform Coding
Sub-image size selection, blocking
DCT implementation using FFT
Run length coding.

## Slide 65: Image Compression
Image compression is art and science of reducing amount of data required to represent the image.
Need for image compression ?
To reduce the storage space
To reduce the transmission time while web surfing
Fundamentals:
Data compression refers to the process of reducing the amount of data required to represent the given information
Data and information are not same
Data is a mean to convey the information
W.k.t. same information can be represented using various amount of data
Some representations may contain irrelevant or repeated information – redundant data

## Slide 66: Image Compression
Let there be two representations to of the same information and let a and b be the number of bits to represent them respectively.
The relative data redundancy RD is given by,
where CR is compression ratio, given by CR= a/b
Based on a and b values there can be three different cases
i. If b = a, no redundant data is present in first set
ii. If b << a, highly redundant data is present in first set.
iii. If b >> a, highly redundant data is present in second set.

## Slide 67: Image Compression
In image compression context, a in the equation for CR, usually is the number of bits needed to represent an image as 2-D array of intensities
Typically 2-D array of intensities suffer from three types of redundancies
  Coding Redundancy
  Spatial or temporal redundancy
  Irrelevant information
Coding Redundancy:
Code- a system of symbols to represent body of information
Each piece of info is assigned with sequence of code symbols called as code words
Number of symbols in each code word is – length
The 8-bit codes that are used to represent the intensities in most of the 2-D intensity arrays contain more bits than needed to represent the intensities

## Slide 68: Image Compression
Spatial or temporal redundancy
Most of the pixels in 2-D intensity arrays are correlated spatially (each pixel is similar to dependent on neighboring pixels) info is unnecessarily replicated in the representation of correlated pixels
Irrelevant information
Most of the 2-D intensity arrays contain information that is ignored by the human visual system or is extraneous to the use of the image.
Hence they can be called as redundant as they are not used
Image compression means eliminating one or more redundancy in the image

## Slide 69: Image Compression
Coding redundancy
Let us assume that, a discrete random variable rk, in the interval [0, L-1] is used to represent the intensities of an MXN image and that each rk, occurs with probability of pr(rk)
Then we can write ….(1)
Where L is number of intensity values and nk is number of occurrences of kth intensity
If no. of bits used to represent each value of rk is l(rk), then average no. of bits needed to represent each pixel is given by
…….(2)
Average length of code word assigned to various intensity values is given by the sum of product of no. of bits used represent each intensity and their probability of occurrences
Total no. of bits needed to represent MXN image is MNLavg.

## Slide 70: Image Compression
If the intensities are represented using m-bit fixed length code the RHS of the previous equation reduces to m, while substituting l(rk) = m.
By taking constant m out of summation we are left with only summation of pr(rk) which is always 1
Consider the following computer generated 256 X 256 image

## Slide 71: Image Compression
The error between two images f(x,y) and ^(x,y) is given by
The total error between two MxN size images is
The root-mean-square error erms between

## Slide 72: Image Compression
Advantages
Simple and convenient technique to evaluate information loss
Subjective Fidelity Criteria
Since human perception is based on subjective quality, it is more suitable to use subjective fidelity criteria to evaluate the information loss.
Concept:
This method is implemented by showing a ‘typical’ decompressed image to a number of viewers.
Then, their evaluation is averaged to take a decision.
These evaluations may be done using a rating scale or side-by-side comparisons such as excellent, better, same, worse, etc.

## Slide 73: Image Compression
Input image f(x, y) is fed to the encoder, which gives the compressed version of image.
This will be stored for later use or transmitted for storage
When the compressed image is given to decoder, a reconstructed output f^(x,y) will be generated
If this is exact replica of f(x, y) then such a compression system is called lossless or error free system.
If not, reconstructed image will be distorted and such a system is called lossy system
Encoding or compression process:

## Slide 74: Image Compression
The encoder is designed to remove the redundancies through three operations one by one
The first stage is mapper stage, which transforms f(x, y) into a format designed to reduce the spatial and temporal redundancy
  This operation is reversible and may or may not reduce the amount of data required to represent the image
  Run-length coding is an example of mapping function
The second stage is quantizer.
  This reduces the accuracy of the mapper’s output in accordance with the pre- established fidelity criterion
  Goal is to keep irrelevant information out of the compression
  Note that this is irreversible operation and hence to be skipped if error-free compression is needed

## Slide 75: Image Compression
Third stage is symbol coder.
  This generates fixed or variable length code to represent the quantizer output and maps the output in accordance with the code.
  In most of the cases, variable length code is used
  Shortest code words are assigned to most frequently occurring quantizer output values.
  This reduces the coding redundancy

## Slide 76: Image Compression
Decoding process:
Decoder consists of two components – symbol decoder and inverse mapper
They perform inverse operations of symbol coder and mapper
Since quantization is irreversible process, reverse of this is not shown in decoding process

## Slide 77: Image Compression
Error Free Compression / Lossless Compression:
Error-free compression is the acceptable data reduction method since there is no data loss.
This method is applicable to both binary and gray-scale images.
It provides compression ratios ranging from 2 to 10.
Operations:
  (i) Forming an alternative representation for the given image by which its interpixel redundancies are reduced
  (ii) Coding the representation to remove its coding redundancies.
E.g.:
Variable-Length Coding
Bit-Plane coding
LZW Coding
Lossless Predictive Coding

## Slide 78: Image Compression
Types of Compression
Two broad categories
1. Lossless algorithms.
2. Lossy algorithms.

## Slide 79
Variable Length Coding –Bit – Plane Coding Lossless Predictive Coding – Lossy Compression – Lossy Predictive Coding.

## Slide 80
Introduction and Overview
The field of image compression continues to grow at a rapid pace
As we look to the future, the need to store and transmit images will only continue to increase faster than the available capability to process all the data

## Slide 81
Applications that require image compression are many and varied such as:
Internet
Businesses
Multimedia
Satellite imaging
Medical imaging

## Slide 82
Compression algorithm development starts with applications to two-dimensional (2-D) still images
After the 2-D methods are developed, they are often extended to video (motion imaging)
However, we will focus on image compression of single frames of image data

## Slide 83
Image compression involves reducing the size of image data files, while retaining necessary information
Retaining necessary information depends upon the application
Image segmentation methods, which are primarily a data reduction process, can be used for compression

## Slide 84
The reduced file created by the compression process is called the compressed file and is used to reconstruct the image, resulting in the decompressed image
The original image, before any compression is performed, is called the uncompressed image file
The ratio of the original, uncompressed image file and the compressed file is referred to as the compression ratio

## Slide 85
The compression ratio is denoted by:

## Slide 86
The reduction in file size is necessary to meet the bandwidth requirements for many transmission systems, and for the storage requirements in computer databases
Also, the amount of data required for digital images is enormous

## Slide 87
This number is based on the actual transmission rate being the maximum, which is typically not the case due to Internet traffic, overhead bits and transmission errors

## Slide 88
Additionally, considering that a web page might contain more than one of these images, the time it takes is simply too long
For high quality images the required resolution can be much higher than the previous example

## Slide 89
Example 10.1.5 applies maximum data rate to Example 10.1.4

## Slide 90
Now, consider the transmission of video images, where we need multiple frames per second
If we consider just one second of video data that has been digitized at 640x480 pixels per frame, and requiring 15 frames per second for interlaced video, then:

## Slide 91
Waiting 35 seconds for one second’s worth of video is not exactly real time!
Even attempting to transmit uncompressed video over the highest speed Internet connection is impractical
For example: The Japanese Advanced Earth Observing Satellite (ADEOS) transmits image data at the rate of 120 Mbps

## Slide 92
Applications requiring high speed connections such as high definition television, real-time teleconferencing, and transmission of multiband high resolution satellite images, leads us to the conclusion that image compression is not only desirable but necessessary
Key to a successful compression scheme is retaining necessary information

## Slide 93
To understand “retaining necessary information”, we must differentiate between data and information
Data:
For digital images, data refers to the pixel gray level values that correspond to the brightness of a pixel at a point in space
Data are used to convey information, much like the way the alphabet is used to convey information via words

## Slide 94
Information:
Information is an interpretation of the data in a meaningful way
Information is an elusive concept; it can be application specific

## Slide 95
There are two primary types of image compression methods:
Lossless compression methods:
Allows for the exact recreation of the original image data, and can compress complex images to a maximum 1/2 to 1/3 the original size – 2:1 to 3:1 compression ratios
Preserves the data exactly

## Slide 96
Lossy compression methods:
Data loss, original image cannot be re-created exactly
Can compress complex images 10:1 to 50:1 and retain high quality, and 100 to 200 times for lower quality, but acceptable, images

## Slide 97
LOSSLESS COMPRESSION METHODS
No loss of data, decompressed image exactly same as uncompressed image
Medical images or any images used in courts
Lossless compression methods typically provide about a 10% reduction in file size for complex images

## Slide 98
Lossless compression methods can provide substantial compression for simple images
However, lossless compression techniques may be used for both preprocessing and postprocessing in image compression algorithms to obtain the extra 10% compression

## Slide 99
The underlying theory for lossless compression (also called data compaction) comes from the area of communications and information theory, with a mathematical basis in probability theory
One of the most important concepts used is the idea of information content and randomness in data

## Slide 100
Information theory defines information based on the probability of an event, knowledge of an unlikely event has more information than knowledge of a likely event
For example:
The earth will continue to revolve around the sun; little information, 100% probability
An earthquake will occur tomorrow; more info. Less than 100% probability
A matter transporter will be invented in the next 10 years; highly unlikely – low probability, high information content

## Slide 101
This perspective on information is the information theoretic definition and should not be confused with our working definition that requires information in images to be useful, not simply novel
Entropy is the measurement of the average information in an image

## Slide 102
The entropy for an N x N image can be calculated by this equation:

## Slide 103
This measure provides us with a theoretical minimum for the average number of bits per pixel that could be used to code the image
It can also be used as a metric for judging the success of a coding scheme, as it is theoretically optimal

## Slide 106
The two preceding examples (10.2.1 and 10.2.2) illustrate the range of the entropy:
The examples also illustrate the information theory perspective regarding information and randomness
The more randomness that exists in an image, the more evenly distributed the gray levels, and more bits per pixel are required to represent the data

## Slide 107
Figure 10.2-1 Entropy
c) Image after binary threshold,
entropy = 0.976 bpp
a) Original image,
entropy = 7.032 bpp
b) Image after local histogram equalization,
block size 4, entropy = 4.348 bpp

## Slide 108
f) Circle with a radius of 32,
and a linear blur radius of 64,
entropy = 2.030 bpp
d) Circle with a radius of 32,
entropy = 0.283 bpp
e) Circle with a radius of 64,
entropy = 0.716 bpp
Figure 10.2-1 Entropy (contd)

## Slide 109
Figure 10.2.1 depicts that a minimum overall file size will be achieved if a smaller number of bits is used to code the most frequent gray levels
Average number of bits per pixel (Length) in a coder can be measured by the following equation:

## Slide 110
Huffman Coding
The Huffman code, developed by D. Huffman in 1952, is a minimum length code
This means that given the statistical distribution of the gray levels (the histogram), the Huffman algorithm will generate a code that is as close as possible to the minimum bound, the entropy

## Slide 111
The method results in an unequal (or variable) length code, where the size of the code words can vary
For complex images, Huffman coding alone will typically reduce the file by 10% to 50% (1.1:1 to 1.5:1), but this ratio can be improved to 2:1 or 3:1 by preprocessing for irrelevant information removal

## Slide 112
The Huffman algorithm can be described in five steps:
Find the gray level probabilities for the image by finding the histogram
Order the input probabilities (histogram magnitudes) from smallest to largest
Combine the smallest two by addition
GOTO step 2, until only two probabilities are left
By working backward along the tree, generate code by alternating assignment of 0 and 1

## Slide 120
In the example, we observe a 2.0 : 1.9 compression, which is about a 1.05 compression ratio, providing about 5% compression
From the example we can see that the Huffman code is highly dependent on the histogram, so any preprocessing to simplify the histogram will help improve the compression ratio

## Slide 121
Run-Length Coding
Run-length coding (RLC) works by counting adjacent pixels with the same gray level value called the run-length, which is then encoded and stored
RLC works best for binary, two-valued, images

## Slide 122
RLC can also work with complex images that have been preprocessed by thresholding to reduce the number of gray levels to two
RLC can be implemented in various ways, but the first step is to define the required parameters
Horizontal RLC (counting along the rows) or vertical RLC (counting along the columns) can be used

## Slide 123
In basic horizontal RLC, the number of bits used for the encoding depends on the number of pixels in a row
If the row has 2n pixels, then the required number of bits is n, so that a run that is the length of the entire row can be encoded

## Slide 124
The next step is to define a convention for the first RLC number in a row – does it represent a run of 0's or 1's?

## Slide 127
Bitplane-RLC : A technique which involves extension of basic RLC method to gray level images, by applying basic RLC to each bit-plane independently
For each binary digit in the gray level value, an image plane is created, and this image plane (a string of 0's and 1's) is then encoded using RLC

## Slide 129
Typical compression ratios of 0.5 to 1.2 are achieved with complex 8-bit monochrome images
Thus without further processing, this is not a good compression technique for complex images
Bitplane-RLC is most useful for simple images, such as graphics files, where much higher compression ratios are achieved

## Slide 130
The compression results using this method can be improved by preprocessing to reduce the number of gray levels, but then the compression is not lossless
With lossless bitplane RLC we can improve the compression results by taking our original pixel data (in natural code) and mapping it to a Gray code (named after Frank Gray), where adjacent numbers differ in only one bit

## Slide 131
As the adjacent pixel values are highly correlated, adjacent pixel values tend to be relatively close in gray level value, and this can be problematic for RLC

## Slide 132
Arithmetic Coding
Arithmetic coding transforms input data into a single floating point number between 0 and 1
There is not a direct correspondence between the code and the individual pixel values

## Slide 133
As each input symbol (pixel value) is read the precision required for the number becomes greater
As the images are very large and the precision of digital computers is finite, the entire image must be divided into small subimages to be encoded

## Slide 134
Arithmetic coding uses the probability distribution of the data (histogram), so it can theoretically achieve the maximum compression specified by the entropy
It works by successively subdividing the interval between 0 and 1, based on the placement of the current pixel value in the probability distribution

## Slide 138
In practice, this technique may be used as part of an image compression scheme, but is impractical to use alone
It is one of the options available in the JPEG standard

## Slide 139
Lossy Compression Methods
Lossy compression methods are required to achieve high compression ratios with complex images
They provides tradeoffs between image quality and degree of compression, which allows the compression algorithm to be customized to the application

## Slide 141
With more advanced methods, images can be compressed 10 to 20 times with virtually no visible information loss, and 30 to 50 times with minimal degradation
Newer techniques, such as JPEG2000, can achieve reasonably good image quality with compression ratios as high as 100 to 200
Image enhancement and restoration techniques can be combined with lossy compression schemes to improve the appearance of the decompressed image

## Slide 142
In general, a higher compression ratio results in a poorer image, but the results are highly image dependent – application specific
Lossy compression can be performed in both the spatial and transform domains.
  Hybrid methods use both domains.

## Slide 143
Gray-Level Run Length Coding
The RLC technique can also be used for lossy image compression, by reducing the number of gray levels, and then applying standard RLC techniques
As with the lossless techniques, preprocessing by Gray code mapping will improve the compression ratio

## Slide 144
Figure 10.3-2 Lossy Bitplane Run Length Coding
Note: No compression occurs until reduction to 5 bits/pixel
b) Image after reduction to 7 bits/pixel,
128 gray levels, compression ratio 0.55,
with Gray code preprocessing 0.66
a) Original image, 8 bits/pixel,
256 gray levels

## Slide 145
Figure 10.3-2 Lossy Bitplane Run Length Coding (contd)
d) Image after reduction to 5 bits/pixel,
32 gray levels, compression ratio 1.20,
with Gray code preprocessing 1.60
c) Image after reduction to 6 bits/pixel,
64 gray levels, compression ratio 0.77,
with Gray code preprocessing 0.97

## Slide 146
Figure 10.3-2 Lossy Bitplane Run Length Coding (contd)
f) Image after reduction to 3 bits/pixel,
8 gray levels, compression ratio 4.86,
with Gray code preprocessing 5.82
e) Image after reduction to 4 bits/pixel,
16 gray levels, compression ratio 2.17,
with Gray code preprocessing 2.79

## Slide 147
Figure 10.3-2 Lossy Bitplane Run Length Coding (contd)
h) Image after reduction to 1 bit/pixel,
2 gray levels, compression ratio 44.46,
with Gray code preprocessing 44.46
g) Image after reduction to 2 bits/pixel,
4 gray levels, compression ratio 13.18,
with Gray code preprocessing 15.44

## Slide 148
A more sophisticated method is dynamic window-based RLC
This algorithm relaxes the criterion of the runs being the same value and allows for the runs to fall within a gray level range, called the dynamic window range
This range is dynamic because it starts out larger than the actual gray level window range, and maximum and minimum values are narrowed down to the actual range as each pixel value is encountered

## Slide 149
This process continues until a pixel is found out of the actual range
The image is encoded with two values, one for the run length and one to approximate the gray level value of the run
This approximation can simply be the average of all the gray level values in the run

## Slide 153
This particular algorithm also uses some preprocessing to allow for the run-length mapping to be coded so that a run can be any length and is not constrained by the length of a row

## Slide 154
Lossy predictive coding
(Differential Predictive Coding)
Differential predictive coding (DPC) predicts the next pixel value based on previous values, and encodes the difference between predicted and actual value – the error signal
This technique takes advantage of the fact that adjacent pixels are highly correlated, except at object boundaries

## Slide 155
Typically the difference, or error, will be small which minimizes the number of bits required for compressed file
This error is then quantized, to further reduce the data and to optimize visual results, and can then be coded

## Slide 157
From the block diagram, we have the following:
The prediction equation is typically a function of the previous pixel(s), and can also include global or application-specific information

## Slide 159
This quantized error can be encoded using a lossless encoder, such as a Huffman coder
It should be noted that it is important that the predictor uses the same values during both compression and decompression; specifically the reconstructed values and not the original values

## Slide 162
The prediction equation can be one-dimensional or two-dimensional, that is, it can be based on previous values in the current row only, or on previous rows also
The following prediction equations are typical examples of those used in practice, with the first being one-dimensional and the next two being two-dimensional:

## Slide 165
Encoder and Decoder